## Slide 1: Chapter 8-2 Memory Model for Program Execution & the Stack
计算机系统概论A
Introduction to Computing Systems
（ CS1002A.01 ）
苗付友
mfy@ustc.edu.cn 2025 Fall
计算机科学与技术学院
School of Computer Science and Technology

## Slide 2
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
Review
1
3
The Stack
2
Memory Model for Program Execution
3
A Machine Structure：von Neumann Model
4
Implementing Functions in C Using a Stack

## Slide 3
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
Review
1
3
The Stack
2
Memory Model for Program Execution
3
A Machine Structure：von Neumann Model
4
Implementing Functions in C Using a Stack

## Slide 4: Review: The Call/Return Mechanism

## Slide 5: Review: Control Instructions for Subroutines
1
1
1
1
0
0
0
0
TrapVector8
TRAP
0
0
0
0
n
z
p
PCoffset9
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
0
0
1
PCoffset11
0
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
BR
JSRR
RTI
JSR
1
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
JMP
1
1
0
0
0
0
0
1
1
1
0
0
0
0
0
0
RET

## Slide 6: Review: Memory in Von Neumann Model

## Slide 7: Review: Using Memory
Memory
  Just a big “array”
  “Indexed” by address
  Accessed with loads and stores
LD/LDR/LDI
  Read a word out of memory
  Use different addressing mode
ST/STR/STI
  Place a word in memory
  Use different addressing mode

## Slide 8: Review: Using Memory
Problem
  What if the memory you want to access is far away?
  LD/ST won’t work (PC-relative)
  LDR/STR won’t work alone (need to get address in register)
Solution:LDI/STI
  Place address of far away value nearby
  Load address, then load/store from that

## Slide 9: Today: Memory Model for Function Calls

## Slide 10
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
Review
1
3
The Stack
2
Memory Model for Program Execution
3
A Machine Structure：von Neumann Model
4
Implementing Functions in C Using a Stack

## Slide 11: Problem
How do we allocate memory during the execution of a program written in C?
  Programs need memory for code and data such as instructions, global and local variables, etc.
  Modern programming practices encourage many (reusable) functions, callable from anywhere.
  Some memory can be statically allocated, since the size and type is known at compile time.
  Some memory must be allocated dynamically, size and type is unknown at compile time. e.g., Declare a list with unknown length.

## Slide 12: Motivation
Why is memory allocation important?
  Allocation affects the performance and memory usage of every C, C++, Java program.
  Current systems do not have enough registers to store everything that is required.
  Static allocation of memory resources is too inflexible and inefficient, as we will see.

## Slide 13: Goals
What do we care about?
  Fast program execution
  Efficient memory usage
  Avoid memory fragmentation
  Maintain data locality
  Allow recursive calls
  Support parallel execution
  Minimize resource allocation
  Memory should never be allocated for functions that are not executed.

## Slide 14: Memory Model in the LC-3
PC
R4(Global pointer)
R6 (stack pointer)
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
R5 (frame pointer)
R5
Function2
R6
R5
R6
Function3
Function1
R5
R6

## Slide 15
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
Review
1
3
The Stack
2
Memory Model for Program Execution
3
A Machine Structure：von Neumann Model
4
Implementing Functions in C Using a Stack

## Slide 16: Stack: An Abstract Data Type
An important abstraction that you will encounter in many applications.
The fundamental model for execution of C, Java, Fortran, and many other languages.
We will describe two applications of the stack:
  Evaluating arithmetic expressions
    Store intermediate results on stack instead of in registers
  Function calls
    Store parameters, return values, return address, dynamic link
    Interrupt-Driven I/O
    Store processor state for currently executing program

## Slide 17: Stack Data Structure
A LIFO (last-in first-out) storage structure
  The first thing you put in is the last thing you take out
  The last thing you put in is the first thing you take out
  This means of access is what defines a stack, not the specific implementation.
Two main operations
  PUSH: add an item to the stack
  POP: remove an item from the stack
Error conditions:
  Underflow (try to pop from empty stack)
  Overflow (try to push onto full stack)
A register (eg. R6) holds address of top of stack (TOS)

## Slide 18: A Physical Stack
Coin holder
Last quarter in is the first quarter out (LIFO)
1995
1996
1998
1982
1995
1998
1982
1995
Initial State
After
One Push
After Three
More Pushes
After
One Pop

## Slide 19: A Hardware Stack Implementation
Data items move between registers
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
Yes
Empty:
TOP
#18
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
No
Empty:
TOP
#12
#5
#31
#18
/ / / / / /
No
Empty:
TOP
#31
#18
/ / / / / /
/ / / / / /
/ / / / / /
No
Empty:
TOP
Initial State
After
One Push
After Three
More Pushes
After
Two Pops

## Slide 20: A Software Stack Implementation
Data items don't move in memory, just our idea about where TOP of the stack is
By convention, R6 holds the Top of Stack (TOS) Pointer (SP)
x3FFF
x4000
x4001
x4002
x4003
x4004
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
#18
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
#18
#31
#5
#12
/ / / / / /
TOP
#18
#31
#5
#12
/ / / / / /
TOP
Initial State
After
One Push
After Three
More Pushes
After
Two Pops
x3FFF
x4000
x4003
x4001
R6
R6
R6
R6

## Slide 21: Basic Push and Pop Code
Note: Stacks can grow in either direction (toward higher address or toward lower addresses)
PUSH
ADD R6, R6, #1 ; increment stack ptr STR R0, R6, #0 ; store data(R0) to TOS
POP
LDR R0, R6, #0 ; load data(R0) from TOS ADD R6, R6, #-1 ; decrement stack ptr
x3FFF
x4000
x4001
X4002
X4003
X4004
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
#18
/ / / / / /
/ / / / / /
/ / / / / /
/ / / / / /
TOP
#18
#31
#5
#12
/ / / / / /
TOP
#18
#31
#5
#12
/ / / / / /
TOP
x3FFF
x4000
x4003
x4001
R6
R6
R6
R6

## Slide 22: Pop with Underflow Detection
If we try to pop too many items off the stack, an underflow condition occurs.
  Check for underflow by checking TOS before removing data.
  Return status code in R5 (0 for success, 1 for underflow)
POP LD R1, EMPTY ADD R2, R6, R1 ; Compare stack pointer BRz UNDER ; with x3FFF LDR R0, R6, #0 ; The actual ‘pop’ ADD R6, R6, #-1 ; Adjust stack pointer AND R5, R5, #0 ; Success: return R5 = 0 RET UNDER AND R5, R5, #0 ; Underflow: return R5 = 1 ADD R5, R5, #1 RET EMPTY .FILL xC001 ; EMPTY = -x3FFF

## Slide 23: Push with Overflow Detection
If we try to push too many items onto the stack, an overflow condition occurs.
  Check for overflow by checking TOS before adding data.
  Return status code in R5 (0 for success, 1 for overflow)
PUSH LD R1, FULL ADD R2, R6, R1 ; Compare stack pointer BRz OVER ; with x4004 ADD R6, R6, #1 ; Adjust stack pointer
STR R0, R6, #0 ; The actual ‘push’ AND R5, R5, #0 ; Success: return R5 = 0 RET OVER AND R5, R5, #0
ADD R5, R5, #1 ; Overflow: return R5 = 1 RET FULL .FILL xBFFC ; FULL = -x4004

## Slide 24: PUSH & POP in LC-3 - 1
POP ST R2,Sv2 ; save, needed by POP
ST R1,Sv1 ; save, needed by POP
LD R1, EMPTY ; EMPTY contains –x3FFF ADD R2, R6, R1 ; Compare stack pointer with x3FFF BRz Fail_exit ; Branch if stack empty LDR R0, R6, #0 ; The actual ‘pop’ to R0 ADD R6, R6, #-1 ; Adjust stack pointer RET EMPTY .FILL xC001 ; EMPTY = -x3FFF
PUSH ST R2,Sv2 ; save, needed by PUSH
ST R1,Sv1 ; save, needed by PUSH
LD R1, FULL ADD R2, R6, R1 ; Compare stack pointer BRz Fail_exit ; with x4004 ADD R6, R6, #1 ; Adjust stack pointer
STR R0, R6, #0 ; The actual ‘push’ RET FULL .FILL xBFFC ; FULL = -x4004

## Slide 25: PUSH & POP in LC-3 - 3
Sv1 .FILL x0000
Sv2 .FILL x0000
Success_exit LD R1, Sv1 ;Restore reg values
LD R2, Sv2 ;
AND R5, R5, #0 ; Success: return R5 = 0 RET
;
Fail_exit LD R1, Sv1 ;Restore reg values
LD R2, Sv2
AND R5, R5, #0
ADD R5, R5, #1 ; Overflow: return R5 = 1 RET

## Slide 26: Arithmetic Using a Stack
Instead of registers, some ISA's use a stack for source and destination operations: a zero-address machine.
  Example: ADD instruction pops two numbers from the stack,adds them, and pushes the result to the stack.
  ADD vs. ADD R0,R1,R2
Evaluating (A+B)·(C+D) using a stack:
push A push B ADD push C push D ADD MULTIPLY pop result
x3FFA
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP

## Slide 27: (25+17) x (3+2)
25
x3FFB
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
25
17
x3FFC
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
42
17
x3FFB
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
42
3
x3FFC
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
42
3
2
x3FFD
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
42
5
2
x3FFC
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
210
5
2
x3FFB
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP
210
5
2
x3FFA
x3FFB
x3FFC
x3FFD
x3FFE
x3FFF
x3FFA
SP

## Slide 28
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
Review
1
3
The Stack
2
Memory Model for Program Execution
3
A Machine Structure：von Neumann Model
4
Implementing Functions in C Using a Stack

## Slide 29: Function in C
Smaller, simpler, subcomponent of program
Provides abstraction
  hide low-level details
  give high-level structure to programer, easier to understand overall program flow
  enables separable, independent development
C functions
  zero or multiple arguments passed in
  single result returned (optional)
  return value is always a particular type
In other languages, called procedures, subroutines, ...

## Slide 30: Example of High-Level Structure
main() { SetupBoard(); /* place pieces on board */ DetermineSides(); /* choose black/white */
/* Play game */ do { WhitesTurn(); BlacksTurn(); } while (NoOutcomeYet()); }
Structure of program is evident, even without knowing implementation.

## Slide 31: Functions in C
Declaration (also called prototype)
int Factorial(int n);
Function call -- used in expression
a = x + Factorial(f + g);
type of return value
name of function
types of all arguments
1. evaluate arguments
2. execute function
3. use return value in expression

## Slide 32: Function Definition
State type, name, types of arguments
  must match function declaration
  give name to each argument (doesn't have to match declaration)
int Factorial(int n)
{
int i; int result = 1; for (i = 1; i <= n; i++) result *= i; return result;
}
gives control back to calling function and returns value

## Slide 33: Why Declaration?
Since function definition also includes return and argument types, why is declaration needed?
Use might be seen before definition.
  Compiler needs to know return and arg types and number of arguments.
Definition might be in a different file, written by a different programmer.
  include a "header" file with function declarations only
  compile separately, link together to make executable

## Slide 34: Example
double ValueInDollars(double amount, double rate);
main() { ... dollars = ValueInDollars(francs, DOLLARS_PER_FRANC); printf("%f francs equals %f dollars.\n", francs, dollars); ...
}
double ValueInDollars(double amount, double rate)
{
return amount * rate;
}
declaration
function call (invocation)
definition

## Slide 35: Storage Requirements
Code must be stored in memory so that we can execute the function.
Parameters must be sent from the caller to the callee so that the function receives them.
Local variables for the function must be stored somewhere, is one copy enough?
Return address must be stored so that control can be returned to the caller.
Return values must be sent from the callee to the caller, that’s how results are returned.

## Slide 36: Function Call in C
Consider the following code:
What needs to be stored?
  Code, parameters, local/global variables, return address/values
// main program
Int a = 10;
Int b = 20;
Int c = foo(a,b);
Int foo(int x,int y)
{
Int z;
z= x+y;
return z;
}

## Slide 37: Possible Solution: Mixed Code and Data
Function implementation:
Can construct data section by appending foo_
foo BR foo_begin ;skip over data
foo_rv .BLKW 1 ;return value
foo_ra .BLKW 1 ;return address
foo_paramx .BLKW 1 ;‘x’ parameter
foo_paramy .BLKW 1 ;‘y’ parameter
foo_localz .BLKW 1 ;‘z’ local
foo_begin ST R7, foo_ra ;save return
… ;may invoke other subroutine
LD R7, foo_ra ;restore return
RET

## Slide 38: Possible Solution: Mixed Code and Data
Calling sequence
Code generation is relatively simple.
Few instructions are spent moving data.
ST R1, foo_paramx ; R1 has ‘x’ --pass parameters
ST R2, foo_paramy ; R2 has ‘y’
JSR foo ; Function call
LD R3, foo_rv ; R3 = return value

## Slide 39: Possible Solution: Mixed Code and Data
Advantages:
  Code and data are close together
  Conceptually easy to understand
  Minimizes register usage for variables
  Data persists through life of program
Disadvantages:
  Cannot handle recursion or parallel execution
  Code is vulnerable to self-modification
  Consumes resource for inactive functions

## Slide 40: Possible Solution: Separate Code and Data
Memory allocation
Code for foo() and bar() are somewhere else
Function code call is similar to mixed solution
foo_rv .BLKW 1 ; foo return value
foo_ra .BLKW 1 ; foo return address
foo_paramx .BLKW 1 ; foo ‘x’ parameter
foo_paramy .BLKW 1 ; foo ‘y’ parameter
foo_localz .BLKW 1 ; foo ‘z’ local
bar_rv .BLKW 1 ; bar return value
bar_ra .BLKW 1 ; bar return address
bar_paramw .BLKW 1 ; bar ‘w’ parameter

## Slide 41: Possible Solution: Separate Code and Data
Advantages:
  Code can be marked ‘read only’
  Conceptually easy to understand
  Early Fortran used this scheme
  Data persists through life of program
Disadvantages:
  Cannot handle recursion or parallel execution
  Consumes resource for inactive functions

## Slide 42: Real Solution: Execution Stack
Instructions are stored in code segment
Global data is stored in data segment
Statically allocated memory uses stack
Dynamically allocated memory uses heap
  Code segment is write protected
  Initialized and uninitialized globals
  Heap can be fragmented
  Stack size is usually limited
  Stack can grow either direction (usual convention is down)

## Slide 43: Execution Stack Requirements
Consider what has to happen in a function call:
  Caller must pass parameters to the callee.
  Caller must transfer control to the callee.
  Caller must allocate space for the return value.
  Caller must save the return address.
  Callee requires space for local variables.
  Callee must return control to the caller.
Parameters, return value, return address, and locals are stored on the stack.
The order above determines the responsibility and order of stack operations.

## Slide 44: Execution Stack
What is an execution stack?
  First In, Last Out (FILO) data structure
  PUSH adds data, POP removes data
  Overflow condition: push when stack full
  Underflow condition: pop when stack empty
  Stack grows and shrinks as data is added and removed
  Stack grows downward from the end of memory space
  Function calls allocate a stack frame
  Return cleans up by freeing the stack frame
  Corresponds nicely to nested function calls
  Stack Trace shows current execution (Java/Eclipse)

## Slide 45: Execution Stack
Definition: A stack frame or activation record is the memory required for a function call:
  Stack frame below contains the function that called this function.
  Stack frame above contains the functions which are called from this function.
  Caller pushes parameters.
  Callee allocates the return value, saves the return address, allocates/frees local variables, and stores the return value.
  Locals are accessed by negative offsets from frame pointer.
  Parameters and return value are Return Address accessed by positive offsets.
  Most offsets are small, this explains LDR/STR implementation.
  Base register stores pointer, signed offset accesses both directions.

## Slide 46: Execution Stack
In the previous solutions, the compiler allocated parameters and locals in fixed memory locations.
Using an execution stack means parameters and locals are constantly moving around.
The frame pointer solves this problem by using fixed offsets instead of addresses.
The compiler can generate code using offsets, without knowing where the stack frame will reside.
Frame pointer needs to be saved and restored around function calls. How about the stack pointer?

## Slide 47: Stack Pointers
Clearly we need a variable to store the stack pointer (SP), LC3 assembly uses R6.
Stack execution is ubiquitous, so hardware has a stack pointer, sometimes even instructions.
Problem: stack pointer is difficult to use to access data, since it moves around constantly.
Solution: allocate another variable called a frame pointer (FP), for stack frame, uses R5.
Where should frame pointer point? Our convention sets it to point to the first local variable.

## Slide 48: Implementing Functions in C Using a Execution Stack
Activation record
  information about each function, including arguments and local variables
  stored on run-time stack
Calling function
push new activation record
copy values into arguments
call function
get result from stack
Called function
execute code
put result in activation record
pop activation record from stack
return

## Slide 49: Run-Time Stack
Recall that local variables are stored on the run-time stack
Stack pointer (R6) points to the beginning of a region of memory that stores local variables for the current function
That region of memory is called an activation record
When a new function is called, its activation record is pushed on the stack; when it returns its activation record is popped off of the stack.

## Slide 50: Run-Time Stack
main
Memory
R6
main
Memory
R6
main
Memory
R6
NoName
Before call
During call
After call
Note: Using R6 this way is incompatible with storing interrupt state on the stack.

## Slide 51: Activation Record
int NoName(int a, int b) { int w, x, y; . . . return y; }
Name
Type
Offset
Scope
a
b
w
x
y
int
int
int
int
int
3
4
5
6
7
NoName
NoName
NoName
NoName
NoName
return value
return address
dynamic link
a
b
w
x
y
bookkeeping
locals
args

## Slide 52: Activation Record Bookkeeping
Return value
  always first word in activation record
  holds value returned by function
  allocated even if function does not return a value
Return address
  save pointer to next instruction in calling function
  convenient location to store R7 in case another function (JSR) is called
Dynamic link
  address of previous activation record
  used to pop this activation record from stack

## Slide 53: Calling the Function-allocate activation record, passing args
b = NoName(a, 10);
; store a to 1st argument LDR R0, R6, #3 STR R0, R6, #8
; store 10 to 2nd argument AND R0, R0, #0 ADD R0, R0, #10 STR R0, R6, #9
; store R6 into dynamic link STR R6, R6, #7
; move R6 to start of new record ADD R6, R6, #5
; call subroutine JSR NoName
ret val
ret addr
dyn link
a
b
ret val
ret addr
dyn link
a
b
w
x
y
x3F00
13
x4100
13
10
x4100
R6
Note: Caller needs to know number and type of arguments, doesn't know about local variables.
1
2
3
4
1
2
3
4

## Slide 54: Starting the Callee Function
; store return address STR R7, R6, #1
ret val
ret addr
dyn link
a
b
ret val
ret addr
dyn link
a
b
w
x
y
x3F00
13
x3100
x4100
13
10
x4100
R6
5
5

## Slide 55: Ending the Callee Function
return y;
; copy y into return value LDR R0, R6, #7 STR R0, R6, #0
; load the return address LDR R7, R6, #1
; load the dynamic link
; (pops the activation record) LDR R6, R6, #2
; return control to caller RET
ret val
ret addr
dyn link
a
b
ret val
ret addr
dyn link
a
b
w
x
y
x3F00
13
40
x3100
x4100
13
10
20
30
40
x4100
R6
6
7
8
8

## Slide 56: Resuming the Caller Function
b = NoName(a,10);
; load return value LDR R0, R6, #5 ; store result into b STR R0, R6, #4
ret val
ret addr
dyn link
a
b
ret val
x3F00
13
40
40
x4100
R6
9
10

## Slide 57: Example
/* Function ToUpper: * If the argument is lower case, * return its upper case ASCII value */ char ToUpper(char inchar)
{ int outchar = inchar; if ('a' <= inchar && inchar <= 'z') outchar = inchar - ('a' - 'A'); return outchar; }
Compile this function to LC-3 assembly language.

## Slide 58: Example: LC-3 Code for ToUpper
ToUpper STR R7, R6, #1 ; save return addr LDR R0, R6, #3 ; load parameter (inchar) STR R0, R6, #4 ; initialize outchar LD R1, neg_a ; load -'a' ADD R1, R0, R1 ; inchar - 'a' BRn FALSE ; br if inchar < 'a' LD R1, neg_z ; load -'z' ADD R1, R0, R1 ; inchar - 'z' BRp FALSE ; br if inchar > 'z' LD R1, neg_upper ; load -('a' - 'A') ADD R0, R0, R1 ; inchar - ('a' - 'A') STR R0, R6, #4 ; store to outchar FALSE LDR R0, R6, #4 ; load outchar STR R0, R6, #0 ; store in result LDR R7, R6, #1 ; load return address LDR R6, R6, #2 ; load dynamic link RET